## Slide 1: Non-Exhaust Emissions, Exposures, and Health Risks from Transportation
Rima Habre, ScD
Associate Professor
Division of Environmental Health & Spatial Sciences Institute
University of Southern California
habre@usc.edu
March 30, 2023
The Long and Winding Road: The Evolution of Mobility – Challenges and Opportunities, Vancouver, BC
Notes: Abstract
Air pollution exposure is the largest environmental risk factor in the global burden of disease, with strong spatial patterning and systemic inequities leading to persistent environmental health disparities. Coupled with climate change and widening gaps in socioeconomic opportunity, these trends are expected to increase over time. While most studies have focused on individual outdoor, regulated criteria air pollutants, humans are exposed to mixtures from various sources with distinct physiochemical properties and toxicity profiles. Furthermore, human mobility, time-activity patterns, and indoor microenvironments contribute significantly to personal exposure and health risk yet are often ignored, introducing exposure measurement error. Advances in geospatial technologies, remote sensing, and personal monitoring have greatly increased our ability to assess highly personalized and source-specific exposures in context, within actual activity spaces, and understand their health effects. This talk will present an overview of these methods and applications from Dr. Habre’s research. The ultimate goal is to advance precision environmental health, design targeted interventions, and reduce health disparities.
Short Bio for Introduction
Dr. Rima Habre is an Associate Professor of Environmental Health and Spatial Sciences at the University of Southern California. Her research aims to understand the effects of co-occurring environmental exposures, air pollution mixtures and social stressors on the health of vulnerable populations across the life course. Dr. Habre co-chairs the Geospatial Working Group in the NIH ECHO Program and is also MPI and Project Lead in the ECHO and MADRES centers at USC, respectively, investigating the effects of neighborhoods, air pollution sources, and mixtures on maternal and child health disparities.

## Slide 2: Non-Exhaust Emissions
Pollutants not emitted from combustion engine, but from wear or degradation of vehicle parts and road surfaces
  Brake wear, tire wear, catalyst wear, road surface wear, road dust resuspension due to turbulence (usually a mix)
  Mainly from friction, erosion, or mechanical abrasion, affected by thermal heat, vehicle weight, weather, driving conditions etc.
  Mostly primary, also contribute to secondary particle formation
  Emitted into air and dust, transported through ecosystem
OECD (2020), Non-exhaust Particulate Emissions from Road Transport: An Ignored Environmental Policy Challenge, OECD Publishing, Paris, https://doi.org/10.1787/4a4dc6ca-en.
Figure from Matthaios et al., STOTEN, 2022

## Slide 3: Non-Exhaust Emissions
Unregulated compared to exhaust emissions
  Sometimes referred to as “non-tailpipe,” doesn’t quite apply for catalyst wear
  Or “Abrasive Vehicular Emissions”
Materials evolving
  Brake pads and discs (low-/semi-metallic, non-asbestos organic, ceramics, etc.)
  Tires (fibers, natural/synthetic rubber, organics, microplastics, etc.)

## Slide 4: Regulatory Evolution of Brake Pad Composition in North America
Taken from Dr. Hiroyuki Hagino’s talk, HEI 2020 Virtual Workshop on Non-Tailpipe Particulate Matter Emissions and Exposure, retrieved from: https://www.healtheffects.org/sites/default/files/hagino-break-wear-particles-emissions.pdf

## Slide 5: Chemical Composition and Source Tracers
OECD (2020), Non-exhaust Particulate Emissions from Road Transport: An Ignored Environmental Policy Challenge, OECD Publishing, Paris, https://doi.org/10.1787/4a4dc6ca-en.

## Slide 6: Chemical Composition and Source Tracers

## Slide 7: Non-Exhaust PM Size Distribution
Larger size fractions (coarse, PM10)
Recent studies showing smaller size ranges too (UFP to PM2.5)
Why does this matter?
  Residence time in air, fate and transport, spatial gradients
  Inhalation exposure potential
Roy and Milton, 2004

## Slide 8: Trends
Studies in US and EU showing decreases in exhaust emissions but increases in non-exhaust emissions
  Relative contribution of non-exhaust to total increasing
  Newer materials, regenerative braking in hybrids and EVs ↓ brake wear, but cars heavier, VMT ↑
OECD (2020), Non-exhaust Particulate Emissions from Road Transport: An Ignored Environmental Policy Challenge, OECD Publishing, Paris, https://doi.org/10.1787/4a4dc6ca-en.

## Slide 9: Trends
Farahani et al, Atm Env 2021
  Combustion sources overall (incl. vehicular exhaust) ↓ 2005-2018
  Road dust resuspension ↑ in LA 2013-2018
Relative contribution of tire wear source (blue) to Zn concentrations in Los Angeles, CA, 2005-2018

## Slide 10: How Do We Assess Human Exposure?
Source(s)
Concentrations
Exposure
Dose
Effect
Body Boundary
Exposure Assessment
Exhaust and Non-Exhaust Sources (Brake Wear, Tire Wear, etc.)
Overall Mixture and its Components
Measurements and/or Models (e.g. LURs, CTMs, source apportionment models, etc.)

## Slide 11: How Do We Assess Human Exposure?
Source(s)
Concentrations
Exposure
Dose
Effect
Body Boundary
Exposure Assessment
SOURCES
RECEPTORS
Receptor-oriented models
Source-oriented models
Source apportionment models

## Slide 12: Source-Oriented Models Line source dispersion models
Physical dispersion (no chemistry)
  eg, RLINE or CALINE4
  Many inputs, highly space/time resolved.. incl. meteorology, emission factors
Challenges for epi
  Spatiotemporal patterns for tailpipe and non-tailpipe pollutants generally highly correlated

## Slide 13: Receptor-Oriented Models Using outdoor community-based measurements
Speciated PM0.2, PM2.5, PM10
8 CHS communities, 2008-9
Tailpipe and non-tailpipe traffic
  Tailpipe EC, wsOC, isOC, B
  Separate gasoline and diesel sources in PM2.5
  Non-tailpipe brake, tire, and catalyst wear signals Ba, Cu, Mo, Sb, Zn, Pt and Pd

## Slide 14: Receptor-Oriented Models Using outdoor community-based measurements
Habre et al., JAWMA, 2021

## Slide 15
Abrasive Vehicular Emissions in PM0.2 (brake, tire, catalyst wear) ↑ when both intersections and non-FwyHwy NOx ↑, outside of LB and ports/trucks area

## Slide 16: Receptor-Oriented Models Using personal monitoring
https://arcg.is/1y8KHn
www.madres.usc.edu
Story Map
Website

## Slide 17: Personal Exposure Monitoring
RTI microPEM
GPS and EMA apps
EMA
Harvard PEMs
Teflon filters
Sensidyne GilAir Plus pumps
Continuous and integrated methods, paired with GPS and EMA mobile surveys during pregnancy and early postpartum

## Slide 18: Activity Spaces and Personal PM2.5 Exposure
Yan Xu, PhD
Xu Y et al., The Impact of GPS-derived Activity Spaces on Personal PM2.5 Exposures in the MADRES Cohort. Environment Research. 2022.
Association with Personal PM2.5 Exposure

## Slide 19: Sources of Personal PM2.5 Exposure
Sources | Average mass contribution (μg/m3) | Percent Contributions (%)
Secondhand Smoking | 11.7 | 64.2
Crustal | 2.3 | 12.6
Fuel Oil | 2.1 | 11.4
Aged Sea Salt | 0.9 | 4.8
Fresh Sea Salt | 0.8 | 4.5
Traffic | 0.4 | 2.4
Sources identified and characteristic species
Secondhand smoking (BrC, ETS, Br)
Crustal (Al, Ca, Si, Ti)
Fuel Oil (Ni, V)
Aged Sea Salt (Na, Mg, S)
Fresh Sea Salt (Cl, Na, Mg)
Traffic (BC, Ba, Zn)
Yan Xu, PhD
Xu Y et al., Sources of Personal PM2.5 Exposure in the MADRES Pregnancy Cohort. JESEE. In Submission.

## Slide 20: Traffic Source
Yan Xu, PhD
Xu Y et al., Sources of Personal PM2.5 Exposure in the MADRES Pregnancy Cohort. JESEE. In Submission.

## Slide 21: Health Risks of Non-Exhaust Emissions
Very well-established epidemiological literature on traffic-related air pollution effects on respiratory and cardiovascular health, mortality, etc.
  Mostly on exhaust, much less on non-exhaust exposures!
  Very high source collinearity > hard to separate exhaust from non-exhaust effects
Toxicology pointing to negative effects
  Inflammation, oxidative stress, perturbed immune responses, etc.
  Expect what we already know about PM size considerations to apply
High-risk subpopulations
  Living or working near major roads (homes, schools, low-income housing)
  Commuters and occupational groups (drivers, heavy-duty equipment operators)
  Existing health vulnerability (elderly, immunocompromised, pregnancy, infants, etc.)
  Disproportionately impacted EJ communities (eg, warehousing, freight, goods movement corridors, etc.)

## Slide 22: Challenges in Assessing Health Risks

## Slide 23: Conclusions
↑ non-exhaust emissions and contributions
Important EJ concerns
Quickly evolving materials, technologies, and fleet
  Hybrids/EVs, regenerative braking, LDVs and HDVs
  Material science question?
Learning a lot from toxicology studies
  Harder to capture real-world conditions
Great improvements in hybrid modeling approaches and well-known (but not always unique) tracers
  Source collinearity still a great challenge for epi!
Notes: Personal exposure to air pollution and other environmental risk factors is highly variable in space and time and depends on human time-activity and mobility patterns, behaviors, indoor and outdoor sources. Especially in large population studies, personal exposure to air pollution is often approximated by static, outdoor residential concentrations predicted with varying degrees of spatiotemporal resolution and accuracy. This talk will demonstrate how advances in personal monitoring and geospatial technologies are allowing researchers to assess highly personalized and spatiotemporally resolved exposures within actual activity spaces to inform precision environmental health. These advances ultimately lead to a better understanding of contextual effects, temporality, and important microenvironments driving adverse exposures and health effects. They also significantly reduce exposure measurement error and amplify statistical power to detect relevant exposure-health associations.

## Slide 24: Thank You
Funding
  LA DREAMERs ECHO Center, NIH UH3OD023287 (Breton, Bastain, Farzan, Habre)
  MADRES Center, NIMHD/NIEHS P50ES026086, NIMHD P50MD015705, EPA RD-83615801 (Breton and Bastain)
  Southern California Environmental Health Sciences Center, NIEHS P30ES007048 (Habre pilot)
  CTSI UL1TR001855 pilot (Habre and Mason)
  NIEHS R01ES027409 (Breton)
Contact Rima Habre, ScD habre@usc.edu
@RimaHabre_ScD
@MadresCenter
@USCEnviroHealth
@USC_SSI

## Slide 25: Materials in Brake Linings and Tires
e.g., 6PDD-quinone compound in tire wear known ecotoxicant (coho salmon)

## Slide 26: Receptor-Oriented Models Using outdoor community-based measurements
Habre et al., JAWMA, 2021
Spearman Correlations, excluding LB data

## Slide 27: Guiding Questions
Aside from exhaust, what are other sources of air pollution from motor vehicles?
How do non-exhaust emissions differ from exhaust emissions?
What do we know about the population health impacts of non-exhaust emissions? Are there specific at-risk groups?
What measures are available to us to help reduce these types of emissions?

## Slide 28: Outline
Non-exhaust vs exhaust emissions from motor vehicles
  Key characteristics
    Sources (brake, tire, road surface wear, road dust)
    Chemistry, size distribution, spatial gradients, temporal profiles, trends
Exposure assessment approaches and challenges
  Modeling (LURs, etc.)
  Source apportionment (line source dispersion models, receptor models)
    ICV2 analysis, others
  Measurements of concentrations vs exposures
    Ambient vs near-road vs on-road
    Outdoor, indoor, personal
  Challenges with source collinearity – what does this mean for epi?
Population health impacts
  What do we know from tox or epi studies
  Specific at-risk groups
Emissions reduction strategies
  Reformulated materials (tire pads/discs, road surfaces, etc.)
  Street washing/cleaning – not very effective
  Hybrid/EV fleet changes, regenerative braking, and expected future trends
  Real-world conditions?