## Slide 1: Air Pollution in Public Transit Systems: Characterization and Mitigation
Keith Van Ryswyk
Senior Indoor Air Quality Researcher
Air Pollution Exposure Science Section, Water and Air Quality Bureau
Health Canada
BC Lung Foundation
Air Quality and Health Workshop 2023

## Slide 2: Overview
2
The Characterization and Mitigation of Air Pollution in Public Transit
Air Pollution Exposure Across Transit Methods
  Active transit
  Complexities of comparing air pollution exposures across transit methods
Improving air pollution in public transit systems
  The Urban Transportation Exposure Study
  Bus Transit: impact of fuel emission standards and propulsion systems
  Subway Transit: Health Canada’s Guidance for Improving Subway Air Quality

## Slide 3: Air Pollution Exposure Across Transit Methods
3
The Characterization and Mitigation of Air Pollution in Public Transit
Cepeda, M., Schoufour, J., Freak-Poli, R., Koolhaas, C. M., Dhana, K., Bramer, W. M., & Franco, O. H. (2017). Levels of ambient air pollution according to mode of transport: a systematic review. The Lancet Public Health, 2(1), e23–e34. https://doi.org/10.1016/S2468-2667(16)30021-4
Mueller, N., Rojas-Rueda, D., Cole-Hunter, T., de Nazelle, A., Dons, E., Gerike, R., Götschi, T., Int Panis, L., Kahlmeier, S., & Nieuwenhuijsen, M. (2015). Health impact assessment of active transportation: A systematic review. Preventive Medicine, 76, 103–114. https://doi.org/10.1016/j.ypmed.2015.04.010
Active Transit Methods
  AT methods: cycling, running, walking
  can increase:
    Transit time
    Proximity to traffic sources
    Breathing rate
  Benefits of physical activity outweigh health risks of increased exposure/dose
    Mueller et al., 2015 & Cepeda, et al., 2017
Motorized Transit Methods
  MT methods: private vehicles and public transit (buses and subways)
  Determinants of exposure can be nation or city-specific

## Slide 4: Air Pollution Exposure Across Transit Methods
4
The Characterization and Mitigation of Air Pollution in Public Transit
Research Comparing Air Pollution Exposures of Transit Methods
Heterogeneity in findings across studies
Ventilation
  Private car recirculation, cabin filtration, mechanical ventilation in subways
Route selection / network design
  distance from traffic congestion
  separation of bus/cyclist lanes
  proportion of rail transit lines below- (BG) and above-grade (AG)
Propulsion types (i.e. diesel, electric, hybrid)
Built environment
Regional ambient air pollution and vehicle emission standards
Indoor air quality standards (i.e. Indoor Air Quality Act)

## Slide 5: Health Canada’s Urban Transportation Exposure Study
5
The Characterization and Mitigation of Air Pollution in Public Transit
Weichenthal, S., Van Ryswyk, K., Kulka, R., Sun, L., Wallace, L., & Joseph, L. (2015). In-vehicle exposures to particulate air pollution in Canadian metropolitan areas: the urban transportation exposure study. Environmental Science & Technology, 49(1), 597–605.
Van Ryswyk, K., Evans, G. J., Kulka, R., Sun, L., Sabaliauskas, K., Rouleau, M., Anastasopolos, A. T., Wallace, L., & Weichenthal, S. (2021). Personal exposures to traffic-related air pollution in three Canadian bus transit systems: the Urban Transportation Exposure Study. Journal of Exposure Science & Environmental Epidemiology, 31(4), 628–640.
Van Ryswyk, K., Anastasopolos, A. T., Evans, G., Sun, L., Sabaliauskas, K., Kulka, R., Wallace, L., & Weichenthal, S. (2017). Metro commuter exposures to particulate air pollution and PM2. 5-associated elements in three
Canadian cities: the urban transportation exposure study. Environmental Science & Technology, 51(10), 5713–5720.
Private Vehicles:
Vancouver, Toronto, & Montreal
Rail Transit:
Vancouver, Toronto, & Montreal
Bus Transit:
Vancouver, Toronto, & Ottawa
System-wide characterization
Pollutants:
NO2
PM2.5
PM10
UFP
BC
Estimating contribution to daily air pollution exposure
Identification of determinants of air pollution variability
Objectives

## Slide 6: Air Quality in Public Transit Systems: Buses
6
The Characterization and Mitigation of Air Pollution in Public Transit
Estimating the impact of bus propulsion type on in-bus air pollution
Buses categorized by propulsion and make year groups
  Diesel: Pre 2004: referent condition
  Diesel: 2004-2006: emission standards introduced in 2004 targeted the reduction of NOx emissions
  Diesel: 2007-: 10-fold improvement in emission standards
  Hybrid diesel/electric
  Electric: Trolley buses (Vancouver only)
Benefits of reducing bus emissions to bus air quality
  2007- diesel class: lower PM2.5, BC, & UFP in all three cities
  Similar improvements for hybrid diesel/electric
Sources of in-bus air pollution
  ~60-70% of daily exposure to PM2.5-Fe and PM2.5-Ba
  Diesel exhaust and brake dust
Van Ryswyk, K., Evans, G. J., Kulka, R., Sun, L., Sabaliauskas, K., Rouleau, M., Anastasopolos, A. T., Wallace, L., & Weichenthal, S. (2021). Personal exposures to traffic-related air pollution in three Canadian bus transit systems: the Urban Transportation Exposure Study. Journal of Exposure Science & Environmental Epidemiology, 31(4), 628–640.
Notes: 2007 diesels employ Diesel particulate filters and selective catalytic reduction systems

## Slide 7: Air Quality in Public Transit Systems: Buses
7
The Characterization and Mitigation of Air Pollution in Public Transit
Electrification of Bus Fleets?
  May results in a significant decrease in diesel exhaust emissions for Canadian cities
  Regenerative braking systems could also reduce the emission of non-exhaust emissions (brake dust)
Zero Emission Transit Fund
  Infrastructure Canada
  Electrification of municipal bus fleets
Municipalities purchasing ‘zero-emission buses’
  Ottawa, Vancouver, Calgary, Winnipeg, and others
https://www.infrastructure.gc.ca/zero-emissions-trans-zero-emissions/index-eng.html

## Slide 8: Air pollution variability by transit method: PM2.5
8
The Characterization and Mitigation of Air Pollution in Public Transit
Montreal
  subway ~ private car
Toronto
  subway >> bus
  subway >> private car
Vancouver
  subway BG > subway AG
  subway AG ~ private car ~ bus
High PM2.5 and PM10 concentrations in BG rail lines reliant on piston-effect for ventilation

## Slide 9: Air Quality in Public Transit Systems: Rail Transit
9
The Characterization and Mitigation of Air Pollution in Public Transit
Van Ryswyk, K.; Anastasopolos, A. T.; Evans, G.; Sun, L.; Sabaliauskas, K.; Kulka, R.; Wallace, L.; Weichenthal, S. Metro Commuter Exposures to Particulate Air Pollution and PM2.5-Associated Elements in Three Canadian Cities: The Urban Transportation Exposure Study. Environ. Sci. Technol. 2017, 51, 5713– 5720, DOI: 10.1021/acs.est.6b05775
Subway commuting’s contribution to daily PM2.5

## Slide 10: Air Quality in Public Transit Systems: Rail Transit
10
The Characterization and Mitigation of Air Pollution in Public Transit
Summer PM2.5
=
½
Winter
PM2.5
continually
operating
ventilation
n=90 units
to ensure thermal comfort

## Slide 11: Air Quality in Public Transit Systems: Rail Transit
11
The Characterization and Mitigation of Air Pollution in Public Transit
Moreno T, de Miguel E. Improving air quality in subway systems: An overview. Environ Pollut. 2018;239:829-831. doi:10.1016/j.envpol.2018.01.077
BG piston-effect-reliant systems (µg/m3)
Toronto: ~140
Stockholm: ~150
London: ~300
Washington DC: ~340
Boston: ~325
New York: ~470
Copenhagen : ~160
PM2.5 Highly enriched in FeO
(London: 47-71%, Toronto: ~75%,
Stockholm & Copenhagen: ~85%)
Extensively below-grade rapid transit rail systems can significantly increase daily PM2.5 for its patrons

## Slide 12: Air Quality in Public Transit Systems: Rail Transit
12
The Characterization and Mitigation of Air Pollution in Public Transit
Van Ryswyk, K., Kulka, R., Marro, L., Yang, D., Toma, E., Mehta, L., McNeil-Taboika, L., and Evans, G., 2021. Impacts of Subway System Modification on Air Quality in Subway Platforms and Trains. Environ. Sci. Tech. 55(16): 11133– 11143.
Data collection
  Gravimetric and Continuous PM2.5
  Lines 1 & 2
  Platform: 2010/11, 2018
  In-Train : 2010/11, 2018, & 2019/20
Results
  Track Bed Vacuuming ineffective at reducing PM2.5
  Newly opened line attained high PM within 1 year
  Estimated impact of high rate of wheel flats and friction brake use
Subway PM2.5
freshly emitted > legacy dust

## Slide 13: Air Quality in Public Transit Systems: Rail Transit
13
The Characterization and Mitigation of Air Pollution in Public Transit
Composition of Subway PM2.5 in Toronto subway (piston-effect reliant ventilation):
Extensively composed of Fe oxides and steel-sourced elements
contribution to Subway PM2.5
system sources >>> outdoor sources

## Slide 14: Air Quality in Public Transit Systems: Rail Transit
14
The Characterization and Mitigation of Air Pollution in Public Transit
Subway Components
Frame A: view of track bed from platform with running and contract ’third’ rails.
Fame B: close up of train bogie with brake and wheel contact.
Frame C: full view of train bogie with wheels, brake pads, and contact shoe.

## Slide 15: Air Quality in Public Transit Systems: Rail Transit
15
The Characterization and Mitigation of Air Pollution in Public Transit
Two-Source Chemical Mass Balance Model
Fe-dominated components
  Wheels, rails, contact rails, and contact shoes
  >94% Fe
Brake pads: Fe, Ba, Cr, Sr
Line 1:
  Mainly sourced by steel components
  Regenerative braking:
  engages at 5km/h
Line 2:
  Even contribution of sources
  High rate of friction brake use

## Slide 16: Air Quality in Public Transit Systems: Rail Transit
16
The Characterization and Mitigation of Air Pollution in Public Transit
Forced ventilation systems
  operating forced mechanical ventilation systems
  automation based on train schedules
In-train filtration
  potentially more effective relative to platform filtration
  commuters spend the majority of their time within subway trains.
Monitoring subway air quality
  identifies the seasons and stations with higher PM concentrations
  can inform strategies to improve subway air quality
Reducing Subway PM emissions
  reducing friction brake use
  performing an audit of the wear and replacement rates of subway components

## Slide 17: Air Quality in Public Transit Systems: Rail Transit
17
The Characterization and Mitigation of Air Pollution in Public Transit
Platform Screen Doors (PSDs).
  PSDs have been installed in many systems for their safety benefits
  effective at reducing platform PM by restricting air flow from tunnels
  can result in an increase of PM in trains and thus overall passenger exposure
Vacuuming and washing
  intervention studies have found limited impact of vacuuming and washing on improving system air quality.
Health Canada. Guidance For Improving Subway Air Quality. March 2022. ISBN: 978-0-660-42505-4. https://www.canada.ca/content/dam/hc-sc/documents/programs/guidance-for-improving-subway-air-quality/subway-guidance-en.pdf

## Slide 18: Summary
18
The Characterization and Mitigation of Air Pollution in Public Transit
Active Transit
  Benefits of physical activity outweigh health risks of increased exposure/dose
Comparing Air Quality Across Modes
  Complicated by factors of city, system, and regulatory factors
Improving Air Quality in Public Transit
  Reducing the emission of traffic-related air pollution
    key for the betterment of air quality in all modes
  Increased use of active transit + public transit
    decreased private vehicle use = decreased traffic congestion = increased urban air quality
  Ongoing electrification of bus transit fleets
Air pollution in below-grade rail transit (subways)
  A unique PM source and composition profile
  Unknown health effects
  Reductions in PM concentrations are possible

## Slide 19: Acknowledgements
19
The Characterization and Mitigation of Air Pollution in Public Transit
Health Canada: Ryan Kulka, Angelos Anastosopoulos, Morgan MacNeill, Hongyu You, Tim Shin, Lui Sun, Scott Weichenthal
University of Toronto: Greg Evans, Cheol Jeong
National Research Council: Elton Toma
Imperial College London: David Green
Copenhagen University: Hugo Russell

## Slide 20: Air pollution variability by transit method: NO2
20
The Characterization and Mitigation of Air Pollution in Public Transit
Montreal (subway = Metro)
  Lower NO2 in subway
  100% below-grade (BG)
  electrical propulsion
Toronto
  Lower NO2 in subway
  ~80% BG
  electrical propulsion
  private car ~ bus
Vancouver (subway = SkyTrain)
  high NO2 variability in subway
  ~80/20% AG/BG Similar levels
  private car ~ bus

## Slide 21: Air pollution variability by transit method: Black Carbon
21
The Characterization and Mitigation of Air Pollution in Public Transit
Subways
  no black carbon data
  High content of Fe Oxides
  Not true representation of BC
Bus vs Private car
  Comparable between methods
  Some variability between methods by city

## Slide 22: Air pollution variability by transit method: UFP (PM0.1)
22
The Characterization and Mitigation of Air Pollution in Public Transit
Subway
below grade (BG)
above grade (AG)
Montreal
  Private vehicle > subway
  Continual ventilation in subway
Toronto
  Private vehicle > bus > BG subway
  subway is unventilated
  ‘piston-effect’ driven
Vancouver
  Private vehicle > bus ~ subway